## Slide 1
Fundamentals of Quantitative Design and Analysis
ADVANCED COMPUTER SYSTEM & ARCHITECTURE
Assoc Prof Mohd Shahizan Othman

## Slide 2: Computer Technology
Performance improvements:
  Improvements in semiconductor technology
    Feature size, clock speed
  Improvements in computer architectures
    Enabled by HLL compilers, UNIX
    Lead to RISC architectures
  Together have enabled:
    Lightweight computers
    Productivity-based managed/interpreted programming languages

## Slide 3: History of Computer Technology

## Slide 4
Historical Microprocessor Performance
Source: H&P textbook

## Slide 5: Classes of Computers
Personal Mobile Device (PMD)
  e.g. start phones, tablet computers
  Emphasis on energy efficiency and real-time
Desktop Computing
  Emphasis on price-performance
Servers
  Emphasis on availability, scalability, throughput
Clusters / Warehouse Scale Computers
  Used for “Software as a Service (SaaS)”
  Emphasis on availability and price-performance
  Sub-class: Supercomputers, emphasis: floating-point performance and fast internal networks
Internet of Things/Embedded Computers
  Emphasis: price

## Slide 7
Processor Technology Trends
Transistor density increases by 35% per year and die size
increases by 10-20% per year… more functionality
Transistor speed improves linearly with size (complex
equation involving voltages, resistances, capacitances)
Wire delays do not scale down at the same rate as logic delays
The power wall: it is not possible to consistently run at
higher frequencies without hitting power/thermal limits;
fancy cooling required beyond ~150W

## Slide 10
Trends in Transistor Count within CPU

## Slide 11
In a clock cycle, can do more work -- since transistors are
faster, transistors are more energy-efficient, and there’s
more of them
Better architectures: finding more parallelism in one thread,
better branch prediction, better cache policies, better
memory organizations, more thread-level parallelism,
moving computations to memory, accelerating some kernels, …
What Helps Performance?

## Slide 12
The 52% growth per year is because of faster clock speeds
and architectural innovations (led to 25x higher speed)
Clock speed increases have dropped to 1% per year in
recent years
The 22% growth includes the parallelization from multiple
cores
Moore’s Law: transistors on a chip double every 18-24 months
Points to Note

## Slide 13: Defining Computer Architecture
“Old” view of computer architecture:
  Instruction Set Architecture (ISA) design
  i.e. decisions regarding:
    registers, memory addressing, addressing modes, instruction operands, available operations, control flow instructions, instruction encoding
“Real” computer architecture:
  Specific requirements of the target machine
  Design to maximize performance within constraints: cost, power, and availability
  Includes ISA, microarchitecture, hardware

## Slide 14: Trends in Technology
Integrated circuit technology (Moore’s Law)
  Transistor density: 35%/year
  Die size: 10-20%/year
  Integration overall: 40-55%/year
DRAM capacity: 25-40%/year (slowing)
  8 Gb (2014), 16 Gb (2019), possibly no 32 Gb
Flash capacity: 50-60%/year
  8-10X cheaper/bit than DRAM
Magnetic disk capacity: recently slowed to 5%/year
  Density increases may no longer be possible, maybe increase from 7 to 9 platters
  8-10X cheaper/bit then Flash
  200-300X cheaper/bit than DRAM

## Slide 15: Bandwidth and Latency
Bandwidth or throughput
  Total work done in a given time
  32,000-40,000X improvement for processors
  300-1200X improvement for memory and disks
Latency or response time
  Time between start and completion of an event
  50-90X improvement for processors
  6-8X improvement for memory and disks

## Slide 16
Copyright © 2019, Elsevier Inc. All rights reserved.
Bandwidth and Latency
Log-log plot of bandwidth and latency milestones

## Slide 17: Transistors and Wires
Feature size
  Minimum size of transistor or wire in x or y dimension
  10 microns in 1971 to .011 microns in 2017
  Transistor performance scales linearly
    Wire delay does not improve with feature size!
  Integration density scales quadratically

## Slide 18: Power and Energy
Problem: Get power in, get power out
Thermal Design Power (TDP)
  Characterizes sustained power consumption
  Used as target for power supply and cooling system
  Lower than peak power (1.5X higher), higher than average power consumption
Clock rate can be reduced dynamically to limit power consumption
Energy per task is often a better measurement

## Slide 19
Clock Speed Increases
Source: H&P textbook

## Slide 20: Reducing Power
Techniques for reducing power:
  Do nothing well
  Dynamic Voltage-Frequency Scaling
    e.g, AMD Opteron
  Low power state for DRAM, disks
    sleep mode
  Overclocking, turning off cores
    Intel i7, AMD Ryzen

## Slide 21
Recent Microprocessor Trends
2004
2010
Source: Micron University Symp.
Transistors: 1.43x / year
Cores: 1.2 - 1.4x
Performance: 1.15x
Frequency: 1.05x
Power: 1.04x

## Slide 22: Integrated Circuit Cost
Integrated circuit
Bose-Einstein formula:
Defects per unit area = 0.016-0.057 defects per square cm (2010)
N = process-complexity factor = 11.5-15.5 (40 nm, 2010)

## Slide 23
More Diverse Platforms
Image credits: uber, extremetech, anandtech

## Slide 24: Principles of Computer Design
Take Advantage of Parallelism
  e.g. multiple processors, disks, memory banks, pipelining, multiple functional units
Principle of Locality
  Reuse of data and instructions
Focus on the Common Case
  Amdahl’s Law

## Slide 25: Principles of Computer Design
The Processor Performance Equation

## Slide 26: Principles of Computer Design
Different instruction types having different CPIs

## Slide 27: Principles of Computer Design
Different instruction types having different CPIs

## Slide 28: Fallacies and Pitfalls
All exponential laws must come to an end
  Dennard scaling (constant power density)
    Stopped by threshold voltage
  Disk capacity
    30-100% per year to 5% per year
  Moore’s Law
    Most visible with DRAM capacity
    ITRS disbanded
    Only four foundries left producing state-of-the-art logic chips
    11 nm, 3 nm might be the limit

## Slide 29: Fallacies and Pitfalls
Microprocessors are a silver bullet
  Performance is now a programmer’s burden
Falling prey to Amdahl’s Law
A single point of failure
Hardware enhancements that increase performance also improve energy efficiency, or are at worst energy neutral
Benchmarks remain valid indefinitely
  Compiler optimizations target benchmarks

## Slide 30
Modern trends:
Clock speed improvements are slowing (power constraints)
Difficult to further optimize a single core for performance
Multi-cores: each new processor generation will accommodate more cores
Need better programming models and efficient execution for multi-threaded applications
Need better memory hierarchies
Need greater energy efficiency
Reduced data movement
Emergence of new metrics: security, reliability
Emergence of new workloads: ML, graphs, genomics
Where Are We Headed?